##### PLASTIC LENS RX LAB WORK

1) Toric Surface Machines (processing concave surface):

| Item | Type | Machine or tools | Unit | QTY | Remark |
| --- | --- | --- | --- | --- | --- |
| Blocking | AB47 | Alloy blocker (47℃) | set | 1 |  |
| Generating | TG80 | Toric generator (cc) | set | 1 | Concave |
| Lapping | TP80.2 | Toric lapping machine | set | 1-2 |  |
| Polishing | TP80.2 | Toric polishing machine | set | 2-4 |  |
| Deblocking | AD | Alloy deblocker | set | 1 |  |
| Lap cutting | TC90 | Toric lap cutter | set | 1 | (Optional) |
| Measuring | TL | Torometer | pc | 1 |  |
|  | SL | Spherometer | pc | 1 |  |
|  | TM | Thickness measurer | pc | 1 |  |
|  |  | Auto lensmeter | pc | 1 |  |
| Tools |  | Blocking ring | pc | some |  |
|  |  | Generating block | pc | some |  |
|  |  | Aluminum lap tool | pc | more |  |
|  |  | located block | pc | 1 |  |
| other |  | Air gun | pc | 3-6 |  |
|  |  | Chiller | pc | 2-4 | (User) |
|  |  | Air compressor | pc | 1 |  |

2).Consumable Material:

| Item | Type | Materials | Unit | QTY | Remark |
| --- | --- | --- | --- | --- | --- |
| Blocking | 47℃ | Blocking alloy | kg |  |  |
|  |  | Surface saver tape | roll |  |  |
| Lapping |  | 1st fining pad | roll |  | (500pcs/roll) |
|  |  | 2nd fining pad | roll |  | (500pcs/roll) |
| Polishing |  | Polishing pad | roll |  | (250pcs/roll) |
|  |  | Polishing polish | gallon |  | (3.78L/gallon) |

Remark:

1. The quantity of machines is based on user’s lens output.

2. Toric Surface Machines (concave surface) can make semi-finished single vision lens to spherical lens or cylinder lens.

3. Toric Surface Machines (concave surface) can make semi-finished round-bifocal/ top-bifocal lens to round-bifocal/ top-bifocal lens.

4. Toric Surface Machines (concave surface) can make semi-finished progressive lens to progressive lens.